## Slide 1
New reinjection technologies in hydrocarbon fields
Ravenna, 28 March 2008

## Slide 2: AA WATER INJECTION – PROJECT SCOPE
Testing of a new re-injection technique in natural gas reservoirs near Ravenna (Angela-Angelina field), in order to
  Improve produced water management
  Mitigate potential subsidence effects
  Have a positive side-effect on reservoir, through pressure maintenance effects
Testing a novel and environmentally friendly system of coastal stabilization (R.S.A.:Recupero e Stabilizzazione Arenili, i.e. Shores Recovery and Stabilization))

## Slide 3: Project genesis
The project has been launched as a part of an Agreement Protocol signed on 12th October 2002 among Regione Emilia Romagna, Province of Ravenna, Municipality of Ravenna and ENI, having as goal an experimental activity of water re-injection in Angelina 1 well (onshore, phase I)
The Agreement Protocol has been renewed on 26th April 2006, with the intent to get more ambitious results, both in terms of reinjected flowrate and location of injection wells (offshore, phase II)
From the very beginning the project has been monitored and supervised by a Techincal Committee of experts and technicians, that include representatives of 2° University of Naples, University of Ferrara, Regione ER, Province and Municipality of Ravenna. The role of the Committee has been confirmed with the renewal of the Protocol

## Slide 4: Project location

## Slide 5: Reinjection sites
ANGELA-ANGELINA
PLATFORM
ANGELINA 1 WELL (CURRENT INJECTION)
2,36 Km
CLUSTER ANGELA
(FUTURE INJECTION)

## Slide 6: Water injection in Oil & gas business
Reinjection of produced water in oil reservoirs dates back to the thirties; it has been adopted in oder to enhance oil recovery and reduce environmental impact.
It spread around in different countries starting from the 70’s
The goal of ENI’s reinjection project is to contrast possible subsidence effects at the surface, and is to be considered as the first experience in Italy and Europe

## Slide 7: Phase I – Onshore reinjection
In 2002 Angelina 1 well has been modified in order to convert it to an injection well.
Starting from March 2003, produced water (early injection phase) has been injected in dedicated levels; up to December 2007 a volume of 171,232 m3 has been injected
Sea water injection started on January 2006, in other levels of Angelina 1 well, and up to December 2007 a total volume of 34,598 m3 of sea water has been put into the reservoir
Both produced water and seawater injection are still going on at the time being

## Slide 8: Reservoir pressure monitoring
ANGELA-ANGELINA
PLATFORM
ANGELINA 1
WELL
2,2 Km

## Slide 9: Phase I – Pressure maintenance effects
Static pressure trend has been monitored through dedicated tests.
Measurements performed in Angelina 1 demonstrated that a sensible increse has taken place nearby the well, due to injection activity
Offshore measurements showed an interesting trend, though available data don’t allow valuable scientific evaluations

## Slide 10: R.S.A. system
The system has been patented in 1985 by Danish Geotechnical Institute, with the acronymous B.M.S. (Beach Management System). The scope was the stabilization of coastal area subject to erosion.
SHORE
WAVES
SEA BOTTOM
BEFORE
AFTER
DRAINING SYSTEM
SEA WATER DOWN FLOW
AVERAGE SEA WATER LEVEL
The system is part of the phase I of the project under discussion. Installed in 2004, it currently supplies sea water for onshore reinjection.

## Slide 11: Digging out in Lido Adriano

## Slide 12: Draining pipes during laying on the shore

## Slide 13: Draining test

## Slide 14: R.S.A. monitoring activity
Starting from March 2004, Consorzio Ferrara Ricerche has been charged with the monitoring activity of R.S.A. performance and its impact on shore profile
Monitoring activity includes registration of sea weather parameters, control of phreatic surface, tracing of morfologic profiles of the emersed/submersed shore. Collected data are periodically transmitted to the members of Agreement Protocol.

## Slide 15: Depositional effect at R.S.A. site
A net depositional effect has taken place, especially during 2007

## Slide 16: Phase II – Offshore injection
A new and bigger coastal protection system (R.S.A.) will be installed in Lido di Dante beach
The system will make available 2500 m3/d of sea water. This flowrate is deemed to ensure a proper shore stabilization and an effective pressure maintenance effect
Water will be filtered and treated, then carried to Angela 2 and Angela 4 injection wells (located in Cluster Angela, near offshore Ravenna) through existing sealines

## Slide 17: RSA (same as BMS) layout at Lido di Dante
C AREA POZZO ANGELINA 1
Pipe laied through telecontrolled horizontal drilling (TOC)
Draining pipes
Sea water collection pits with pumps
Confluence pit
LIDO DI DANTE
LIDO ADRIANO
Angelina 1 well